## Slide 1: Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products Along with Major Geometrical Properties
Seyed Muhammad Hossein Mousavi S. Muhammad Hassan Mosavi Tehran, Iran
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021), October 28-29, 2021, Ferdowsi University of Mashhad

## Slide 2: Goals:
Decreases human error and saves more time
Using color and depth image (Kinect V.2)
In irregular and non-symmetrical shaped fruits
In different distance from sensor
Extracting 10 color and depth image features
Fast response in real time calculation
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
2

## Slide 3: Introduction
Better health care leads to more population.
More population means more source of food.
As demand increases, it lifts up the supply.
Modern tools to plant, harvest, quality evaluation and packaging are required.
In quality evaluation part, product grading plays an important role in quality management.
Volume and mass estimation are part of product grading process.
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
3

## Slide 4: Introduction (Traditional Methods)
Traditional volume estimation method is Water Displacement method (WD).
So time consuming and damages the products.
Does not calculate exact amount of volume in agricultural products in different shapes (irregular and non-symmetrical).
Higher final error.
Traditional mass estimation method is called Digital Balance (DB) method.
Time consuming and effects the freshness of the product.
To fix could use heavy machinery.
But it is so costly and required more space.
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
4

## Slide 5: Introduction (Traditional Methods)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
5
(a) using traditional WD method on a carrot sample (volume) and (b) using traditional digital balance method for the same carrot (mass)

## Slide 6: Introduction (Novel Methods)
Computer vision techniques had impact in agricultural product processes.
One of the best impacts is in grading process like volume and mass estimation.
There are decent color image-based techniques in order to do that.
But with some issues.
Proposed method lifts up the existing methods to a level higher.
Improve in precision, different distances and also in pure darkness aspects.
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
6

## Slide 7: Introduction (Kinect V.2)
Kinect is one of the most famous depth sensors.
It is low-cost and available out there.
Employs night vision technology.
Works based on infrared particles in decent quality and resolution.
Is proper for both research purposes and in application.
Main tools for this research is Kinect V.2 sensor.
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
7

## Slide 8: Introduction (Kinect V.2)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
8
Employed Kinect V.2 sensor in the research

## Slide 9: Introduction (Kinect V.2)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
9
(a) is the depth structure shown as an intensity channel of an eggplant vegetable.
The smaller value means closer distance to the sensor and vice versa.
(b) is the standard color (RGB) image of the same eggplant.
Depth image calls 2.5-Dimentional image.
It is possible to convert 2.5-D image into a 3-D image by a simple processing.

## Slide 10: Prior Related Researches
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
10
Jana, Susovan and et al (2020)
Automatic volume and mass estimation of fruits and vegetables.
Using ordinary smartphone color cameras.
System works for irregular and non-axisymmetric products.
Specific distance from sensor.
Potato, tomato and citrus products with 77 samples in total.
Their system did not support pure darkness situation and also in different distances.

## Slide 11: Prior Related Researches
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
11
Vivek Venkatesh, G. et al (2015)
Volume and mass of Axis-Symmetric fruits using color sensors (single view).
They extract the boundary counter.
Then categorized the fruit into circular and elliptical shapes.
Volume is calculated based on the specific fruit in each experiment.
Mass is calculated based on the relationship between mass and volume.
Four types of citruses in validation section (120 samples).
Their system does not support irregular and non-symmetrical shaped products.

## Slide 12: Prior Related Researches
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
12
Mousavi, S.M.H. and Prasath (2019)
Employed Depth sensors (Kinect).
Different product distances of 0.8, 1.0, and 1.3 meters from sensor.
System starts with pre-processing steps.
Estimating the weight using average weight of the experimented product and its distance From sensor plus a constant.
Finally normalization of the final value into gram.
150 samples of Sweet Lemons Sweet Peppers and Tomatoes for validation purposes.
Just estimate fruits weight.

## Slide 13: Proposed Method
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
13
A robust infrared based volume and mass estimation system.
Fruits and vegetables.
Fixes Some issues in available new and traditional methods.
Works on irregular and non-symmetrical shaped fruits.
In different distance from sensor.
Fast response in real time calculation.

## Slide 14: Proposed Method (Pre-processing)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
14
Median filter followed by unsharp mask filter color and depth images.
Helps for smoothing from inside and sharpening from outside.
Canny edge detection filter on color and depth images.
Filling unnecessary holes using closing morphology operation.
Active contour segmentation
Extracting region boundaries
Background extraction

## Slide 15: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
15
Ten 2-D and 3-D features are extracted from color and depth data.
Color data features are:
Length
Width
Diameter
Perimeter
Depth data features are:
Thickness or height
Surface area
Volume
Convex volume
Solidity
Mass

## Slide 16: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
16
Some steps of preprocessing on one of the color sample from proposed database (2-D)

## Slide 17: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
17
Some steps of preprocessing on one of the depth sample from proposed database (3-D)

## Slide 18: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
18
Color data is used to extract 2-D features.
2-D Length, width
Length and width features are axis-pixel count based.
2-D Diameter
Fruits are non-symmetrical and carrot is not circular among other circular ones
So, diameter has different meaning here.
Diameter calculations two biggest axis-pixel value more than zero.
Finally, a straight line in centimeter determines the diameter value.

## Slide 19: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
19
2-D Perimeter
Perimeter is the distance around the boundary of the region around the 2-D shape.
It computes the perimeter by calculating the distance between each adjoining pair of pixels around the border of the region.
In which L is Length, W is Width, D is Diameter and P is Perimeter.

## Slide 20: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
20
3-D Thickness or height
Depth sensor calculates the distance between the sensor and the product.
Might some bumps be on the surface of the sample.
Thickness is highest gray level achieved from the top surface of the sample in depth data.
Data is recording from two sides and each side gives slightly different value of thickness.
The largest amount of two will be selected.

## Slide 21: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
21
3-D Surface area
Due to irregular shapes, it is not possible to use common equations of 3-D surface area.
Subdivide it into familiar shapes and calculate the area of the familiar shapes.
Sum those area calculations to get the area of the irregular shape they make up.
Used 3-D model is mesh type in the research.
So, the model is made of triangular faces.
In which b is the base and h being perpendicular height
final 3-D surface area equation would be:

## Slide 22: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
22
3-D Convex volume and Solidity
Given a set of points in the plane, the convex hull of the set is the smallest convex polygon that contains all points of it.
Now, the convex volume is the volume of the convex hull, which its mesh structure is based on triangular calculations.
A voxel is a raster graphic on a 3-D grid, with the values of length, width and depth.
Proportion of the voxels in the convex hull that are also in the region, returned as a scalar which is computed as volume / convex volume is called Solidity.

## Slide 23: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
23
3-D Volume
3-D models are based on mesh model, which basically made of triangular shapes.
In surface area, it was sum of 2-D tringles area values on the model.
But 2-D shapes have no volume, so triangular prisms make our final 3-D mesh model.
Calculating sum of the 3-D triangular prisms which makes the final model, 3-D volume of the fruit will be calculated.
In which b is the base, h is the height and l are the length.

## Slide 24: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
24
3-D Mass
There is a relation between volume, mass and density.
Having two of them, another one is calculable.
Each matter has its unique density, which agricultural products are not exception.
Garlic has average density of 0.47 g/cm3, carrot’s density is 1.40 g/cm3, potato’s density is 0.63 g/cm3 and quince’s density is 0.91 g/cm3.
The gram per cubic centimeter (g/cm3) is a unit of density defined as mass in grams divided by volume in cubic centimeters.

## Slide 25: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
25
3-D Mass
The relation between density, volume and mass is as:
In which M is mass, D is Density and V is Volume.
3-D features is as:
In which T, S, V, C, S and M are Thickness or height, Surface area, Volume, Convex volume, Solidity and Mass respectively.
So, the final feature vector would be as:

## Slide 26: Proposed Method (Feature extraction)
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
26
3-D features on one of the samples in the experiment

## Slide 27: Proposed Dataset
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
27
Total 60 samples in different shapes.
Axisymmetric, non-axisymmetric, regular shaped and non-regular shaped.
20 Potatoes, 15 Garlics, 15 Carrots and 10 Quinces.
Three Every Day Carry (EDC) LED Bulb 9 w power lights.
Kinect sensor is placed in 0.8-meter from subject (Distance is adjustable).
Windows 10 64-bit operating system along with MATLAB R 2019 b software.

## Slide 28: Proposed Dataset
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
28
Recording setup environment

## Slide 29: Proposed Dataset
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
29
Some samples from proposed dataset

## Slide 30: Validation and Results
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
30
Comparison with proposed, traditional and modern volume and mass estimation.
Error metrics are Mean absolute error (MAE)
It’s the average over the test sample of the absolute differences between prediction and actual observation where all individual differences have equal weight.
Mean Absolute Percentage Error (MAPE)
Statistical measure of how accurate a predict system is.
The average absolute percent error for each time period minus actual values divided by actual values

## Slide 31: Validation and Results
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
31
Linear regression
Attempts to model the relationship between two variables.
One variable is considered to be an explanatory variable.
Other is considered to be a dependent variable.

## Slide 32: Validation and Results
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
32
Comparison results for proposed volume estimation method versus WD method for garlic samples in milliliter
Comparison results for proposed mass estimation method versus DB method for carrot samples in gram

## Slide 33: Validation and Results
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
33
Sample | Volume (ml) – (D = 0.63 g/cm3) |  |  |  |  | Mass (gm) |  |  |  |  | Run time (sec)
Potato | WD | [10] | [2] | [11] | Proposed | DB | [10] | [2] | [11] | Proposed | Proposed
P01 | 462.0 | 453.6 | 447.0 | 474.8 | 466.1 | 291.06 | 285.76 | 281.61 | 299.12 | 293.64 | 0.61
P02 | 317.1 | 308.7 | 302.1 | 329.9 | 318.3 | 199.77 | 194.48 | 190.32 | 207.83 | 200.52 | 0.69
P03 | 252.0 | 243.6 | 237.0 | 264.8 | 256.3 | 158.76 | 153.46 | 149.31 | 166.82 | 161.46 | 0.65
P04 | 342.3 | 333.9 | 327.3 | 355.1 | 347.9 | 215.64 | 210.35 | 206.19 | 223.71 | 219.17 | 0.51
P05 | 333.9 | 325.5 | 318.9 | 346.7 | 340.6 | 210.35 | 205.06 | 200.90 | 218.42 | 214.57 | 0.58
P06 | 212.1 | 203.7 | 197.1 | 224.9 | 218.7 | 133.62 | 128.33 | 124.17 | 141.68 | 137.78 | 0.61
P07 | 602.7 | 594.3 | 587.7 | 615.5 | 608.8 | 379.70 | 374.40 | 370.25 | 387.76 | 383.54 | 0.59
P08 | 632.1 | 623.7 | 617.1 | 644.9 | 635.6 | 398.22 | 392.93 | 388.77 | 406.28 | 400.42 | 0.49
P09 | 651.0 | 642.6 | 636.0 | 663.8 | 653.3 | 410.13 | 404.83 | 400.68 | 418.19 | 411.57 | 0.56
P10 | 854.7 | 846.3 | 839.7 | 867.2 | 856.3 | 538.46 | 533.16 | 529.01 | 546.33 | 539.46 | 0.71
P11 | 235.2 | 226.8 | 220.2 | 248.2 | 236.4 | 148.17 | 142.88 | 138.72 | 156.36 | 148.93 | 0.77
P12 | 300.3 | 291.9 | 285.3 | 313.1 | 302.8 | 189.18 | 183.89 | 179.73 | 197.25 | 190.76 | 0.69
P13 | 317.1 | 308.7 | 302.1 | 329.9 | 323.1 | 199.77 | 194.48 | 190.32 | 207.83 | 203.55 | 0.57
P14 | 585.9 | 577.5 | 570.9 | 598.7 | 592.2 | 369.11 | 363.82 | 359.66 | 377.18 | 373.08 | 0.58
P15 | 537.6 | 529.2 | 522.6 | 550.4 | 539.7 | 338.68 | 333.39 | 329.23 | 346.75 | 340.01 | 0.62
P16 | 392.7 | 384.3 | 377.7 | 405.5 | 400.8 | 247.40 | 242.10 | 237.95 | 255.45 | 252.50 | 0.68
P17 | 342.3 | 333.9 | 327.3 | 355.1 | 347.3 | 215.64 | 210.35 | 206.19 | 223.71 | 218.79 | 0.59
P18 | 535.5 | 527.1 | 520.5 | 548.3 | 538.4 | 337.36 | 332.07 | 327.91 | 345.42 | 339.19 | 0.78
P19 | 363.3 | 354.9 | 348.3 | 376.1 | 366.9 | 228.87 | 223.58 | 219.42 | 236.94 | 231.14 | 0.81
P20 | 758.1 | 749.7 | 743.1 | 770.9 | 759.7 | 477.60 | 472.31 | 468.15 | 485.66 | 478.61 | 0.56
Comparison results for potato samples

## Slide 34: Validation and Results
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
34
Comparison results for garlic samples
Sample | Volume (ml) – (D = 0.47 g/cm3) |  |  |  |  | Mass (gm) |  |  |  |  | Run time (sec)
Garlic | WD | [10] | [2] | [11] | Proposed | DB | [10] | [2] | [11] | Proposed | Proposed
G 01 | 121.3 | 113.6 | 112.1 | 127.1 | 123.0 | 57.01 | 53.39 | 52.69 | 59.74 | 57.81 | 0.51
G 02 | 162.9 | 155.2 | 153.7 | 168.7 | 166.5 | 76.56 | 72.94 | 72.24 | 79.29 | 78.26 | 0.69
G 03 | 153.8 | 146.1 | 144.6 | 159.6 | 157.1 | 72.29 | 68.67 | 67.96 | 75.01 | 73.84 | 0.48
G 04 | 150.1 | 142.4 | 140.9 | 155.9 | 152.9 | 70.55 | 66.93 | 66.22 | 73.27 | 71.86 | 0.53
G 05 | 93.7 | 86.0 | 84.50 | 99.50 | 98.0 | 44.04 | 40.42 | 39.71 | 46.77 | 46.06 | 0.52
G 06 | 114.6 | 106.9 | 105.4 | 120.4 | 117.0 | 53.86 | 50.24 | 49.54 | 56.59 | 54.99 | 0.56
G 07 | 128.1 | 120.4 | 118.9 | 133.9 | 131.9 | 60.21 | 56.59 | 55.88 | 62.93 | 61.99 | 0.57
G 08 | 139.6 | 131.9 | 130.4 | 145.4 | 143.8 | 65.61 | 61.99 | 61.29 | 68.34 | 67.59 | 0.41
G 09 | 187.5 | 179.8 | 178.3 | 193.3 | 191.4 | 88.13 | 84.51 | 83.80 | 90.85 | 89.96 | 0.69
G 10 | 170.0 | 162.3 | 160.8 | 175.8 | 172.2 | 79.90 | 76.28 | 75.58 | 82.63 | 80.93 | 0.71
G 11 | 149.3 | 141.6 | 140.1 | 155.1 | 152.0 | 70.17 | 66.55 | 65.85 | 72.90 | 71.44 | 0.69
G 12 | 125.4 | 117.7 | 116.2 | 131.2 | 126.0 | 58.94 | 55.32 | 54.61 | 61.66 | 59.22 | 0.62
G 13 | 118.9 | 111.2 | 109.7 | 124.7 | 120.8 | 55.88 | 52.26 | 51.56 | 58.61 | 56.78 | 0.61
G 14 | 119.3 | 111.6 | 110.1 | 125.1 | 122.3 | 56.07 | 52.45 | 51.75 | 58.80 | 57.48 | 0.58
G 15 | 168.9 | 161.2 | 159.7 | 174.7 | 172.0 | 79.38 | 75.76 | 75.06 | 82.11 | 80.84 | 0.59

## Slide 35: Validation and Results
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
35
Comparison results for carrot samples
Sample | Volume (ml) – (D = 1.4 g/cm3) |  |  |  |  | Mass (gm) |  |  |  |  | Run time (sec)
Carrot | WD | [10] | [2] | [11] | Proposed | DB | [10] | [2] | [11] | Proposed | Proposed
C 01 | 359.3 | 348.7 | 350.6 | 368.8 | 362.4 | 503.02 | 488.18 | 490.84 | 516.32 | 507.36 | 0.71
C 02 | 346.8 | 336.2 | 338.1 | 356.3 | 351.8 | 485.52 | 470.68 | 473.34 | 498.82 | 492.52 | 0.72
C 03 | 139.2 | 128.6 | 130.5 | 148.7 | 140.5 | 194.88 | 180.04 | 182.70 | 208.18 | 196.70 | 0.89
C 04 | 220.0 | 209.4 | 211.3 | 229.5 | 223.6 | 308.00 | 293.16 | 295.82 | 321.30 | 313.04 | 0.59
C 05 | 170.8 | 160.2 | 162.1 | 180.3 | 175.8 | 239.12 | 224.28 | 226.94 | 252.42 | 246.12 | 0.63
C 06 | 117.6 | 119.0 | 120.9 | 139.1 | 116.7 | 165.44 | 166.60 | 169.26 | 194.74 | 162.78 | 0.69
C 07 | 419.9 | 409.3 | 411.2 | 429.4 | 424.2 | 587.86 | 573.02 | 575.68 | 601.16 | 593.88 | 0.57
C 08 | 536.9 | 526.3 | 528.2 | 546.4 | 538.5 | 751.66 | 736.82 | 739.48 | 764.96 | 753.90 | 0.52
C 09 | 299.6 | 289.0 | 290.9 | 309.1 | 305.3 | 419.44 | 404.60 | 407.26 | 432.74 | 427.42 | 0.67
C 10 | 670.2 | 659.6 | 661.5 | 679.7 | 673.2 | 938.28 | 923.44 | 926.10 | 951.58 | 942.48 | 0.72
C 11 | 689.8 | 679.2 | 681.1 | 699.3 | 694.3 | 965.72 | 950.88 | 953.54 | 979.02 | 972.02 | 0.63
C 12 | 601.0 | 590.4 | 592.3 | 610.5 | 604.7 | 841.40 | 826.56 | 829.22 | 854.70 | 846.58 | 0.64
C 13 | 530.6 | 520.0 | 521.9 | 540.1 | 537.0 | 742.84 | 728.00 | 730.66 | 756.14 | 751.80 | 0.58
C 14 | 465.6 | 455.0 | 456.9 | 475.1 | 469.1 | 651.84 | 637.00 | 639.66 | 665.14 | 656.74 | 0.78
C 15 | 347.4 | 336.8 | 338.7 | 356.9 | 348.3 | 486.36 | 471.52 | 474.18 | 499.66 | 487.62 | 0.70

## Slide 36: Validation and Results
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
36
Comparison results for quince samples
Sample | Volume (ml) – (D = 0.91 g/cm3) |  |  |  |  | Mass (gm) |  |  |  |  | Run time (sec)
Quince | WD | [10] | [2] | [11] | Proposed | DB | [10] | [2] | [11] | Proposed | Proposed
Q 01 | 329.5 | 322.3 | 320.9 | 337.4 | 331.5 | 299.85 | 293.29 | 292.02 | 307.03 | 301.67 | 0.64
Q 02 | 313.3 | 306.1 | 304.7 | 321.2 | 316.9 | 285.10 | 278.55 | 277.28 | 292.29 | 288.38 | 0.59
Q 03 | 269.9 | 262.7 | 261.3 | 277.8 | 271.6 | 245.61 | 239.06 | 237.78 | 252.80 | 247.16 | 0.53
Q 04 | 197.0 | 189.8 | 188.4 | 204.9 | 199.0 | 179.27 | 172.72 | 171.44 | 186.46 | 181.09 | 0.50
Q 05 | 286.3 | 279.1 | 277.7 | 294.2 | 288.2 | 260.53 | 253.98 | 252.71 | 267.72 | 262.26 | 0.56
Q 06 | 225.6 | 218.4 | 217.0 | 233.5 | 229.3 | 205.30 | 198.74 | 197.47 | 212.49 | 208.66 | 0.63
Q 07 | 203.9 | 196.7 | 195.3 | 211.8 | 206.2 | 185.55 | 179.00 | 177.72 | 192.74 | 187.64 | 0.76
Q 08 | 412.6 | 405.4 | 404.0 | 420.5 | 415.3 | 375.47 | 368.91 | 367.64 | 382.66 | 377.92 | 0.70
Q 09 | 568.9 | 561.7 | 560.3 | 576.8 | 571.7 | 517.70 | 511.15 | 509.87 | 524.89 | 520.25 | 0.68
Q 10 | 398.2 | 391.0 | 389.6 | 406.1 | 401.5 | 362.36 | 355.81 | 354.54 | 369.55 | 365.37 | 0.62

## Slide 37: Validation and Results
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
37
Error results for all methods and all samples (volume and mass)
 | Volume |  |  | Mass | 
 | MAE | MAPE |  | MAE | MAPE
Potato | [10] = 8.40 [2] = 15.00 [11] = 12.79 Proposed = 4.06 | [10] = 2.16 [2] = 3.86 [11] = 3.30 Proposed = 1.09 |  | [10] = 5.29 [2] = 9.45 [11] = 8.06 Proposed = 2.56 | [10] = 2.12 [2] = 3.88 [11] = 3.32 Proposed = 1.08
Garlic | [10] = 7.70 [2] = 9.20 [11] = 5.80 Proposed = 2.90 | [10] = 5.67 [2] = 6.77 [11] = 4.27 Proposed = 2.12 |  | [10] = 3.62 [2] = 4.32 [11] = 2.72 Proposed = 1.36 | [10] = 5.61 [2] = 6.75 [11] = 4.22 Proposed = 2.10
Carrot | [10] = 9.98 [2] = 8.34 [11] = 10.30 Proposed = 3.50 | [10] = 3.07 [2] = 2.64 [11] = 3.90 Proposed = 1.04 |  | [10] = 13.92 [2] = 11.62 [11] = 14.36 Proposed = 4.99 | [10] = 3.03 [2] = 2.61 [11] = 3.86 Proposed = 1.10
Quince | [10] = 7.20 [2] = 8.60 [11] = 7.90 Proposed = 2.60 | [10] = 2.48 [2] = 2.96 [11] = 2.72 Proposed = 0.88 |  | [10] = 6.55 [2] = 7.82 [11] = 7.18 Proposed = 2.36 | [10] = 2.48 [2] = 2.97 [11] = 2.72 Proposed = 0.89

## Slide 38: Validation and Results
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
38
Linear regression for potato samples (Proposed vs WD (volume)- Proposed vs DB (mass)- Proposed vs Proposed (volume and mass))

## Slide 39: Conclusion, discussion and suggestions for future works
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
39
Adding depth data to color data, increases the final detection and recognition accuracy.
Kinect sensor is a suitable tool in agricultural product grading.
3-D features plus 2-D features fixes traditional and color-based methods weaknesses.
Single image based and non-learning based, so the runtime speed is high.
Cheap price, so rational to replace this digital system with traditional heavy machinery.
No product damage and no high error in big scales.
Suggested to use more fruits or vegetables with the system.
Suggested to use more than two angles on agricultural products.
Suggested to using more sensors for simultaneous recording.

## Slide 40: References
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
40
Sachdeva, Sandeep, Tilak R. Sachdev, and Ruchi Sachdeva. "Increasing fruit and vegetable consumption: challenges and opportunities." Indian journal of community medicine: official publication of Indian Association of Preventive & Social Medicine 38.4 (2013): 192.
Jana, Susovan, Ranjan Parekh, and Bijan Sarkar. "A De novo approach for automatic volume and mass estimation of fruits and vegetables." Optik 200 (2020): 163443.
Brosnan, Tadhg, and Da-Wen Sun. "Inspection and grading of agricultural and food products by computer vision systems—a review." Computers and electronics in agriculture 36.2-3 (2002): 193-213.
Gupta, Tushar, Mohan Yellishetty, and T. N. Singh. "Measurement of Bulk volume and Density of Irregular Solid Samples by Sand Displacement Method." Rock Mechanics and Rock Engineering 50.3 (2017): 639-645.
Saranya, N., et al. "Fruit Classification Using Traditional Machine Learning and Deep Learning Approach." International Conference On Computational Vision and Bio Inspired Computing. Springer, Cham, 2019.
Cornejo, Jadisha Yarif Ramírez, and Helio Pedrini. "Automatic fruit and vegetable recognition based on CENTRIST and color representation." Iberoamerican Congress on Pattern Recognition. Springer, Cham, 2016.
Mousavi, Seyed Muhammad Hossein, Vyacheslav Lyashenko, and Surya Prasath. "Analysis of a robust edge detection system in different color spaces using color and depth images." Компьютерная оптика 43.4 (2019).
Raheja, J. L., et al. "Robust gesture recognition using Kinect: A comparison between DTW and HMM." Optik 126.11-12 (2015): 1098-1104.
Mousavi, Seyed Muhammad Hossein, and S. Younes Mirinezhad. "Iranian kinect face database (IKFDB): a color-depth based face database collected by kinect v. 2 sensor." SN Applied Sciences 3.1 (2021): 1-17.
Vivek Venkatesh, G., et al. "Estimation of volume and mass of axi-symmetric fruits using image processing technique." International journal of food properties 18.3 (2015): 608-626.

## Slide 41: References
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
41
Liu, Sidong, et al. "Localized sparse code gradient in alzheimer's disease staging." 2013 35th Annual International Conference of the IEEE Engineering in Medicine and Biology Society (EMBC). IEEE, 2013.
Mesbah Oskui, Shirin, et al. "Measuring the mass, volume, and density of microgram-sized objects in fluid." PloS one 12.4 (2017): e0174068.
Maiseli, Baraka Jacob. "Optimum design of chamfer masks using symmetric mean absolute percentage error." EURASIP Journal on Image and Video Processing 2019.1 (2019): 74.
Ahmar, Ansari Saleh. "Sutte Indicator: an approach to predict the direction of stock market movements." arXiv preprint arXiv:1903.11642 (2019).
Bartlett, Peter L., et al. "Benign overfitting in linear regression." Proceedings of the National Academy of Sciences (2020).
Walker, M. L., et al. "An improved boxplot for univariate data." The American Statistician 72.4 (2018): 348-353.
Han, Hua, et al. "Least squares support vector machine (LS-SVM)-based chiller fault diagnosis using fault indicative features." Applied Thermal Engineering 154 (2019): 540-547.
Santiago Jr, Cereneo Sailog, et al. "Development and Evaluation of Portable Oil Density Scale Device." International Journal of Computing Sciences Research 3.3 (2019): 1-12.
Mousavi, Seyed Muhammad Hossein, Vincent Charles, and Tatiana Gherman. "An Evolutionary Pentagon Support Vector Finder Method." Expert Systems with Applications 150 (2020): 113284.
Mousavi, Seyed Muhammad Hossein, S. Younes MiriNezhad, and Atiye Mirmoini. "A new support vector finder method, based on triangular calculations and K-means clustering." 2017 9th International Conference on Information and Knowledge Technology (IKT). IEEE, 2017.

## Slide 42
11th International Conference on Computer and Knowledge Engineering (ICCKE 2021)
Automatic Infrared-Based Volume and Mass Estimation System for Agricultural Products
Thank You so Much for Your Attention.
???